## Slide 2
Embedded Pro-Camp
Oleksandr Kolosov
MCU and periphery
8/31/2018

## Slide 3: Agenda
What is microcontroller?
CPU
Memory
Periphery

## Slide 4
What is microcontroller?

## Slide 5: What is MCU?
CPU
Memory
Peripheral Functions
MCU structure
Photo is example for placement and max. size

## Slide 6
CPU

## Slide 7: Cortex M3 processor
The Cortex-M4 processor is the first ARM processor based on the ARMv7 architecture
The central Cortex-M4 core is based on Harvard architecture
The Cortex-M4 processor is a 32-nit processor, with a 32-bit wide data path, register bank and memory interface
Cortex M3 processor info
Photo is example for placement and max. size

## Slide 8: Cortex M4 core
3 stage pipeline
Thumb and Thumb-2 instruction set
Hardware division support
Single cycle multiplier
Cortex M3 core structure
Photo is example for placement and max. size
Register bank
3-stage pipeline

## Slide 9: Instruction set
ARM instructions are a fixed length of 32 bits
Thumb instructions are a fixed length of 16 bits
Thumb-2 instructions can be ether 16-bit or 32-bit
Thumb-2 gives approximately 26% improvement in code density over ARM
Thumb-2 gives approximately 25% improvement in performance over Thumb

## Slide 10: ARM register bank
User – normal execution mode
FIQ – Fast interrupt mode
IRQ – Interrupt mode
SVC – Supervisor mode
ABT – Memory access failure
UND – Undefined instruction executed
ARM operation modes

## Slide 11: Cortex M3 pipeline

## Slide 12
Memory

## Slide 13: Memory types
Type | Volatile | Writable | Erase size | Max Erase Cycles | Cost | Speed
SRAM | Yes | Yes | Byte | Unlimited | Expensive | Fast
DRAM | Yes | Yes | Byte | Unlimited | Moderate | Moderate
Masked ROM | No | No | n/a | n/a | Inexpensive | Fast
PROM | No | Once (programmer) | n/a | n/a | Moderate | Fast
EPROM | No | Yes (programmer) | Entire Chip | Limited | Moderate | Fast
EEPROM | No | Yes | Byte | Limited | Expensive | Fast to read, slow to write
Flash | No | Yes | Page | Limited | Moderate | Fast to read, slow to write
NVRAM | No | Yes | Byte | Unlimited | Expensive | Fast

## Slide 14: STM32 Memory map

## Slide 15
Periphery

## Slide 16: CMSIS
The Cortex Microcontroller Software Interface Standard (CMSIS) provides a single standard across all Cortex-Mx processor series vendors. It enables code re-use and code sharing across software projects and reduces time-to-market for new embedded application

## Slide 17: Clocking

## Slide 18: GPIO

## Slide 19: Timers

## Slide 20: UART
Full duplex
Asynchronous
Only one pair can be connected
Both devices in pair are equal
CTS and RTS could be used to flow control
UART1
UART2
RX
TX
TX
RX
GND
GND
UART description
P
0
1
Data Bits 5-8
Start bit
Stop bit
Optional parity bit

## Slide 21: SPI
Full duplex
Synchronous
Master/slave relationship
Can be attached multiple devices on same bus.
Very fast
SPI description

## Slide 22: SPI topology
Star topology
Ring topology

## Slide 23: SPI timing diagram

## Slide 24: I2C
Half duplex
Synchronous
Master/slave relationships
Can be attached multiple devices on same bus.
I2C description

## Slide 25
Q&A

## Slide 26: Home task
Ex1: Develop application that communicates with PC trough UART
Application should send just echo.
You should use only CMSIS library.
UART driver should contains following functions:
  init();
  open();
  read();
  write();
  close();
  deinit();

## Slide 27
Thank you